## Slide 1: Ion channels as molecular switches (Patch clamp technique)
Bionanotechnology
BBL 747

## Slide 2: Introduction
The transmission of signals within and between cells is mediated by ion channels, pore-forming proteins embedded in the plasma membranes of nearly all cells.
In sensory organs the channels translate physical or chemical stimuli into electrical signals for the nervous system.
Even cells not connected to the central nervous system, such as those in the blood, immune system, liver and other organs, use ion channels for signaling processes.
Since the 1950s biologists have been able to study the electric currents arising from these ion fluxes at a macroscopic level.
Only since the 1970s, however, could they examine the individual ion channels themselves.
The patch clamp technique, for which the Nobel Prize for Physiology or Medicine was awarded (1991)

## Slide 3
Transport across Cell Membrane
FIGURE: Summary of transporter types. Some types (ionophores, ion channels, and passive transporters) simply speed transmembrane movement of solutes down their electrochemical gradients, whereas others (active transporters) can
pump solutes against a gradient, using ATP or a gradient of a second solute to provide the energy.

## Slide 4: Patch clamp technique
Tight sealing a pipette against the surface of a neuron enables researchers to study the ion channels in the outer plasma membrane.
The pipette, only 1/25,000 the diameter of a human hair, physically and electrically isolates the trapped channels.
This technique, known as patch clamping, can record the opening and closing of ion channels.
The technique is being used to discover the details of signaling networks within cells.

## Slide 5: Patch clamp technique
Although its development and refinement took several years, the technique is fundamentally simple: a thin glass pipette of the proper shape is tightly sealed against a cell membrane, thereby isolating a small patch of the membrane and the ion channels it contains.
These channels can then be chemically or electrically manipulated and their properties deduced.
A researcher can even remove a patch of membrane from a cell or carefully open a window into a living cell to alter its cytoplasmic constituents.
In all these various applications the patch clamp technique makes it possible to probe how ion channels affect membrane voltage and cell processes such as secretion and contraction.

## Slide 6: Three Forms of Patch Clamping
By pressing a patch pipette against the enzymatically cleaned surface of a cell and applying gentle suction, researchers can place a giga ohm seal around a small patch of the cell membrane and the ion channels it contains. An experimenter can then apply various stimuli from within the pipette and measure the behavior ‘Of the trapped channels.
Alternatively, the experimenter may detach the membrane patch from the cell, thereby exposing the cytoplasmic mouth of the channels
If the membrane patch can be ruptured without breaking the giga-ohm seal, the experimenter can alter the constituents of the living cell's cytoplasm.

## Slide 7: Background
Artificial lipid membranes, which in their pure form are electrical insulators. Yet Ross C. Bean and his colleagues demonstrated that if trace quantities of certain antibiotics or proteins were inserted into the membranes, they became electric conductors.
The discrete changes in the current passing through the membranes suggested that the proteins created pore-like channels that opened and closed individually.
Charged ions could then traverse the membrane through the open channels.
It became clear to many investigators that the electrical signals in neurons and other cells must be mediated by similar proteins in the lipid plasma membranes surrounding them.
Alan L. Hodgkin and Andrew F. Huxley had previously invoked the concept of ion channels in their classic analysis of currents through nerve membranes, for which they received the Nobel Prize in 1963.
If measurements at an appropriately fine resolution could be taken, a whole microcosm of signaling molecules would be found.

## Slide 8: Background
In 1972 Bernard Katz and Ricardo Miledi conducted a statistical analysis of voltage fluctuations at the neuromuscular junction (the synapse between a motor neuron and a muscle fiber).
They concluded that the synaptic signals consisted of small electrical events of the same magnitude as those associated with the artificial channels.
But Katz and Miledi could only infer the properties of the channels from their analysis, which depended on several assumptions.
No method was available for directly measuring the unit events constituting the synaptic signal.
The background noise associated with the standard techniques for measuring the electric current passing through a cell membrane was only one ten-billionth of an ampere, but it was 100 times greater than the current of a unit event and drowned out its signal.

## Slide 9: Background
The available electronic components would have the resolution necessary for measurement only if a small patch of membrane could be insulated from the rest.
The approach was to place a glass micropipette onto the surface of enzymatically cleaned muscle fibers.
The nonconductive glass pipette, isolated a few ion channels, thereby providing with a clear signal
Unfortunately, obtaining a tight seal between a measuring glass pipette and a membrane was not easy.
to put up with electrical leaks that connected the extracellular fluid with the interior of the pipette.
Nevertheless, by carefully cleaning the cell surface and by optimizing the shape and size of the pipette, they succeeded in observing individual channel currents in response to acetylcholine, the transmitter (signal-inducing chemical) at the neuromuscular junction

## Slide 10: Background
It confirmed many previous inferences about the elementary currents through ion channels, in particular the assumption that they were pulse-like events with constant amplitudes and varying durations.
The low quality of the pipette-to membrane seal and the attendant background noise initially precluded from making detailed recordings of ion channels other than those found at the neuromuscular junction.
It was discovered that the application of a slight suction through the pipette, together with some other procedural changes, could raise the resistance of the seal to more than a billion ohms-an improvement of several orders of magnitude.
By gently pulling, with the attached pipette, it was even possible to excise microscopic patches of the membrane for study in isolation.
Thereafter, the recording of single ion channels became a high resolution technique.

## Slide 11: Receptor Channels
The most detailed information on the role of ion channels in synaptic transmission has been obtained from experiments on the neuromuscular junction of skeletal muscle.
There the presynaptic neurons release acetylcholine in discrete multimolecular packets called quanta.
Acetylcholine molecules bind transiently to acetylcholine receptor channels, specialized proteins in the postsynaptic membrane, and cause a current to flow across the end-plate membrane.
This end-plate current is the sum of the elementary currents through hundreds of thousands of channels.
To measure these elementary currents individually, one can press the tip of a patch pipette onto a muscle fiber at the end plate.
This region of muscle surface contains the acetylcholine receptor channel.
When a low concentration of acetylcholine is in the pipette solution, the current recorded with the pipette switches between two levels.

## Slide 12: Receptor Channels
At one level, effectively no current flows because all the ion channels in the membrane patch are shut.
When one channel molecule flips to the open state, because of a voltage applied to the membrane, a current of about 2.5 picoamperes abruptly flows through it.
After a variable period, the molecule flips back to the shut state, and the current switches off.
The opening of the receptor channel is triggered by its binding to acetylcholine the unbinding of acetylcholine causes the channel to close again.
The randomness of the lengths of time for which the channel stays open and closed reflects the probabilistic nature of the interactions between the acetylcholine molecules and their receptors.
The amplitude of the current steps represents the capacity of the channel to transport ions, such as sodium or potassium in the case of the acetylcholine receptor channel.